| C1 | Storage in Raw cream tank | 1.1 | Cream goes off because of temperature | Cream cooled and processed promptly |  | Cream < 10C and <12hrs | Process control checks | Process or check acidity development to | Process Tech. | Process Procedures |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 1.2 | Cream goes off because of dirty plant Water required quality Valves pumps and process equipment in good condition | Tank cleaned every 24 hours under set conditions Laboratory tests Engineering repair and maintenance |  | CIP Set correct Water meets potable standards | Checks on process records Investigate, clean and refill system Equipment functioning correctly | Clean before use Engineers Repair all faults and check production | Process Tech. Laboratory Engineers | Process procedures Laboratory procedures Maintenance records |
|  |  | 1.3 | Cream goes off because of damage to vessel | Sound tank integrity |  | No cracked or damaged vessels | Three monthly checks by engineers | Repair damage. Do not use tank | Engineers | Engineers method |
|  |  | 1.4 | Cream contaminated with chemicals such as cleaning fluids | SCADA controlled CIP |  | No cleaning fluid or chemical residues | Compositional checks on cream | Process monitoring and laboratory checks | Process Tech. Laboratory | Laboratory tests schedule |
|  |  | 1.5 | Foreign bodies get into cream | Vessel enclosed | CCP 3 | No ingress of foreign bodies | Process checks | Investigate and reject contaminated product. | Process Tech. | Process Procedures |
| C2 | Cream to Balance Tank | 2.1 | Foreign bodies falling into cream | Covered balance tanks | CCP 3 | No foreign bodies | Audits | Reject milk with foreign bodies | Process Tech. | Lab and Process |
|  |  | 2. 2 | Ingress of water from water line | Fail safe valve |  | No water ingress causing FPD failures | Freezing point test | Ensure FPD in final product is correct | Process Tech. Lab Tech. | Lab and Process |
|  |  | 2.3 | Chemical contamination from cleaning fluids | Fail safe detergent valves |  | No chemical contamination | Organoleptic checks, valve maintenance | Reject milk with chemical contamination | Process Tech. Lab Tech. | Lab and Process |
| C3 | Cream to regenerative heating section | 3.1 | Contamination into finished cream | Plate pack integrity checks and pressure balance system |  | No holes in plates | Annual plate integrity checks. Pressure balance controlled by Pasteurizers | Repair plates Repair pressure balance | Engineers Process Tech. | Process and Engineers |
|  |  | 3.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Tech. Lab Tech. | Lab and Process |
| C4 | Cream through homogeniser | 4.1 | Contamination from dirty plant | CIP & Sterilise after 8 hours running |  | Clean pipe-work | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Tech. Lab Tech. | Lab and Process |
|  |  | 4.2 | Unhomogenised cream (Not usually homogenised) | Correct homogenisation pressure |  | Fat globules <1.5 micron & no trace | Pasteurizer control Laboratory checks | Reject incorrectly homogenised milk | Process Tech Lab Tech. | Lab and Process |
| C5 | Cream regen. heating sections | 5.1 | Contamination with raw cream | Plate pack integrity checks Pressure balance system |  | No holes in plates | Annual plate integrity checks. Pressure balance. | Repair plates Check phosphatase, repair | Engineers | Engineers |
|  |  | 5.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Technicians. Lab Tech. | Lab and Process |
| C6 | Milk through boost pump | 6.1 | Raw cream in finished milk | Boost pump keeps down stream pressure higher than upstream |  | No raw cream in product | Pasteurizer control Tech. checks | Reject product containing raw milk | Process Technicians | Process |
| C7 | Cream through heating section | 7.1 | Contamination with raw cream | Plate pack integrity checks and pressure balance system | CCP4 | No holes in plates | Annual plate integrity checks. Pressure balance controlled by Pasteurizer system. Phosphatase test | Repair plates Repair pressure balance | Engineers | Engineers LiMS |
|  |  | 7.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Tech. Lab Technicians | Lab and Process |
|  |  | 7.3 | Defects due to over-processing or under | Microbial Contamination due to under-processing |  | Heat to >76 (79-81oC) Divert 76oC | Tech. checks | Reject over processed milk | Processing | Process |
| C 8 | Cream through holding tube | 8.1 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Tech. Lab Tech. | Lab and Process |
|  |  | 8.2 | Under-treated or over treated cream | Holding tube the correct length Flow at the correct rate | CCP5 | Holding time 25 – 30 seconds | Check on commissioning or after plant change | Reject milk if below 15 seconds (or customer specification) | Engineering Process Technicians | Engineers Process |
| C 9 | Milk through flow diversion valve | 9.1 | Untreated or over treated cream | Flow diversion system checked daily | CCP5 | Flow diversion operates at 76C | Daily checks Instrument calibrations | Reject milk Adjust calibration | Process Technicians Engineers | Engineers Process |
|  |  | 9.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Tech. Lab Technicians | Lab and Process |
| C 10 | Milk through regenerative cooling | 10.1 | Contamination with raw cream | Plate pack integrity checks and pressure balance system | CCP4 | No holes in plates | Annual plate integrity checks. Pressure balance controlled by Pasteurizer | Repair plates Repair pressure balance | Engineering Process Technicians | Engineers Process |
|  |  | 10.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Technicians. | Process |
| C 11 | Milk through cooling section | 11.1 | Contamination with raw cream | Plate pack integrity checks and pressure balance system | CCP4 | No holes in plates | Annual plate integrity checks. Pressure balance controlled by Pasteurizer. | Repair plates Repair pressure balance | Engineering Process Tech. | Engineers Process |
|  |  | 11.2 | Contamination from Dirty plant | CIP & Sterilise after 8 hours running |  | Clean plant | Pasteurizer control Laboratory checks | Re-clean plant in the event of CIP failure | Process Technicians. | Process |
|  |  | 11.3 | Undercooled cream | Glycol cooling | CCP 10 | Cream <10C | Tech. checks Instrument calibrations | Adjust temperature, recalibrate and reject milk | Engineering Process Technicians | Engineers Process |
| C 12 | Storage in Finished cream tank | 12.1 | Cream goes off because of temperature | Cream cooled and processed promptly | CCP 10 | Cream in tank < 6C and processed within 12 hours | Process control checks | Process or check acidity development to | Process Technicians | Process Procedures |
|  |  | 12.2 | Cream goes off because of dirty plant | Tank cleaned every 24 hours under set conditions | CCP9 | >.5% NaOH <.9% NaOH 80 – 95 C | Checks on process records | Clean before use | Process Technicians | Process procedures |
|  |  |  |  | Valves pumps and process equipment kept in good condition |  | Equipment functioning correctly | Engineering repair and maintenance | Repair all faults and investigate any effected production | Engineers | Maintenance records |
|  |  | 12.3 | Cream goes off because of damage to vessel | Sound tank integrity |  | No cracked or damaged vessels | Three monthly checks by engineers | Repair damage. Do not use tank | Engineers | Engineers method |
|  |  | 12.4 | Cream contaminated with chemicals such as cleaning fluids | SCADA controlled CIP |  | No cleaning fluid or chemical residues | Compositional checks on cream | Process monitoring and laboratory checks | Process Technicians Laboratory | Laboratory tests schedule |
|  |  | 12.5 | Foreign bodies get into cream | Vessel enclosed | CCP 3 | No route for ingress of foreign bodies | Process checks | Investigate and decision appropriate | Process Technicians | Process Procedures |
| C 13 | Filling Tanker | 13.1 | Cream goes off due to contamination from pipe-work and flexi hoses | Lines cleaned every 24 hours under set conditions | CCP 9 | >.5% NaOH <.9% NaOH 80 – 95 C | Checks on process records | Clean before use | Process Tech. | Process procedures |
|  |  |  |  | Valves pumps and process equipment kept in good condition |  | Equipment functioning correctly | Engineering repair and maintenance | Repair all faults and investigate any effected production | Engineers | Maintenance records |
|  |  |  |  | Flexi pipe ends kept in good condition and off floor |  | Pipe clean and in good condition | Good practice and supervision | Re-clean or replace | Process Technicians | Process procedures |
|  |  | 13.2 | Cream goes off because tanker not clean | Cleaned in last 24 hours | CCP9 | Check tanker cleaning record | Records checked | Reject tanker or contact Milk office | Process Technicians | Process Procedures |
| C 14 | Compositional sampling and testing | 14.1 | Microbial contamination from in-line sampler | Sampler cleaned minimum of every 24hrs |  | Equipment functioning correctly | Engineering repair and maintenance | Repair all faults and investigate any effected production | Engineers | Maintenance records |